## digital_input group
This group contains all digital input signals.
Each signal is a sub group with the signal name as the group name.
    "digital_input": {
        "user_button": {
        "pad": "PA3"
        }
    }
### pad
defines the chip pad that the signal should be read from.
type: string
default: no default possible
### invert
If this setting is set to “on” then a Low (Gnd) signal will be read as 1. A High (Vcc) level will be read as 0.
If this setting is set to “off” (=default) then a High (Vcc) signal will be read as 1. A Low (Gnd) level will be read as 0.
type: string
default: “off”
## API
bool name_is_active(void)