# EZ-USB FX2G3
USB 2.0 @ 480MHz (High Speed)
Package: 104 LGA (8x8mm)
Temperaure range: -45 .. 85 °C
Operating Voltage: 1.7V to 3.6 V
GPIF/FIFO 16bit
## Variants
part #	MCU	SRAM	Flash	SCB #	Peripherals
CYUSB2315-BF104AXI(T)	M0+(MPU)@100 MHz	512 KB	256 KB	1	I2C
CYUSB2316-BF104AXI(T)	M0+(MPU)@100 MHz	512 KB	256 KB	3	I2C, SPI, CAN
CYUSB2317-BF104AXI(T)	M0+(MPU)@100 MHz	512 KB	512 KB	6	I2C, SPI, CAN, QSPI
CYUSB2318-BF104AXI(T)	M4(FP,MPU)@150 MHz/M0+(MPU)@100 MHz	1024 KB	512 KB	6	I2C, SPI, CAN, QSPI, Crypto

CY = Cypress
  USB = USB Controller
     2 = USB 2.0
      xxx = part number
        -BF104AX = LGA Package
        I = Industrial
        T = Tape and reel
## Memory Map
start address	end address	used for	comment
0x00 00 00 00	0x01 ff ff ff	Code	Program code region. Data can also be placed here. It includes the exception vector table, which starts at address 0.
0x00 00 00 00	0x00 01 ff ff	ROM	size = 128 kB
0x08 00 00 00	0x08 01 ff ff	SRAM	size = 128 kB
0x10 00 00 00	0x10 07 ff ff	Internal application flash	size = up to 512 kB
0x14 00 00 00	0x14 00 7f ff	Auxiliary flash, can be used for EEPROM Emulation	size = 32 kB
0x16 00 00 00	0x16 00 7f ff	SFlash	size = 32 kB
0x1c 00 00 00	0x1c 0f ff ff	High bandwidth DMA buffer SRAM	size = up to 1 MB
0x20 00 00 00	0x3f ff ff ff	reserved
0x40 00 00 00	0x5f ff ff ff	Peripheral	All peripheral registers. Code cannot be executed from this region. CM4 bit-band in this region is not supported in EZ-USBTM FX2G3.
0x60 00 00 00	0x9f ff ff ff	external RAM	Quad SPI: Code can be executed from this region.
0xA0 00 00 00	0xDf ff ff ff	external device	not used
0xe0 00 00 00	0xe0 0f ff ff	Private Peripheral Bus	Provides access to peripheral registers within the CPU core
0xe0 10 0a 00	0xff ff ff ff	device	device specific system registers

## Pins
- ePad
- A1..A56
- B1..B48
Pin	Signal name	description
ePAD	GND
A1	P0CTL2
A2	P0CTL1
A3	VDDIOXTAL
A4	XTALOUT
A5	XTALIN
A6	GND
A7	V33
A8	DPLUS
A9	DMINUS
A10	GND
A11	VDDD
A12	GND
A13	P0CLK
A14	Reserved
A15	I2C-SCL0 (SCB0)
A15	UART-RX0 (SCB0)
A16	I2C-SDA0 (SCB0)
A16	UART-TX0 (SCB0)
A17	VDDIO
A18	P0D0
A19	P0D1
A20	P0D2
A21	P0D3
A22	P0D4
A23	P0D5
A24	P0D6
A25	P0D7
A26	GND
A27	VDDIOP0_CTRL
A28	GND
A29	P0CTL5
A30	P0CTL6
A31	P0CTL9
A32	VDDIOP0
A33	GPIO2
A33	UART-TX0
A33	I2C-SDA0 (SCB5)
A33	SPI-CS0 (SCB5)
A33	CAN1-RX
A34	PMODE
A34	SPI-MOSI (SCB5)
A34	CAN1-TX
A35	P0CTL0
A36	GPIO1
A36	UART-RX0
A36	I2C-SCL0 (SCB5)
A36	SPICLK (SCB5)
A37	P0CTL3
A38	P0CTL4
A39	P0CTL7
A40	P0CTL8
A41	GND
A42	XRES
A43	VDDIOP0_CTRL
A44	VBUSDETECTN
A45	P0D8
A46	P0D9
A47	P0D10
A48	P0D11
A49	P0D12
A50	P0D13
A51	P0D14
A52	P0D15
A53	GND
A54	CLKOUT
A55	VDDIOP0
A56	GND
B1	DNU
B2	DNU
B3	DNU
B4	DNU
B5	DNU
B6	DNU
B7	DNU
B8	GND
B9	DNU
B10	DNU
B11	DNU
B12	DNU
B13	DNU
B14	RESREF
B15	TDO / SWO
B15	PDM3-CLK0
B15	UART-TX1 (SCB4)
B15	I2C-SCL1 (SCB4)
B15	SPICLK (SCB4)
B16	TDI
B16	PDM3-DATA0
B16	UART-RX1 (SCB4)
B16	I2C-SDA1 (SCB4)
B16	SPICS0 (SCB4)
B17	TMS / SWDIO
B17	PDM3-CLK1
B17	UART-RTS1 (SCB4)
B17	SPI-MOSI (SCB4)
B18	TCLKSWDCLK
B18	PDM3-DATA1
B18	UART-CTS1 (SCB4)
B18	SPI-MISO (SCB4)
B19	GPIO
B19	SWDRST
B20	PDMDATA
B20	TCPWM4_N
B21	GPIO4
B21	SPI-MISO (SCB5)
B22	SPICLK (SMIF)
B22	UART-RX1 (SCB6)
B22	I2C-SCL1 (SCB6)
B23	SPICS0 (SMIF)
B23	UART-TX1 (SCB6)
B23	I2C-SDA1 (SCB6)
B24	SPICS1 (SMIF)
B25	CAN0-TX
B25	PDM0-DATA1
B25	UART-TX0 (SCB4)
B25	I2C-SDA0 (SCB4)
B25	TCPWM2_N
B25	SPICS0 (SCB4)
B26	CAN0-RX
B26	PDM0-CLK1
B26	UART-RX0 (SCB4)
B26	I2C-SCL0 (SCB4)
B26	TCPWM2_P
B26	SPICLK (SCB4)
B27	SPIDAT0 (SMIF)
B27	UART-RX1 (SCB0)
B27	I2C-SCL (SCB0)
B27	SPICLK (SCB2)
B28	SPIDAT1 (SMIF)
B28	UART-TX1 (SCB0)
B28	I2C-SDA (SCB0)
B28	SPICS0 (SCB2)
B29	SPIDAT2 (SMIF)
B29	UART-CTS0 (SCB0)
B29	SPI-MOSI (SCB2)
B30	SPIDAT3 (SMIF)
B30	UART-RTS0 (SCB0)
B30	SPI-MISO (SCB2)
B31	VDDIOQSPI
B32	SPIDAT4 (SMIF)
B32	UART-CTS0 (SCB2)
B33	SPIDAT5 (SMIF)
B34	SPIDAT6 (SMIF)
B34	UART-RX1 (SCB1)
B34	I2C-SDA1 (SCB1)
B35	SPIDAT7 (SMIF)
B35	UART-TX1 (SCB1)
B35	I2C-SCL1 (SCB1)
B36	DNU
B37	DNU
B38	GPIO5
B39	GPIO6
B40	VCCD
B41	DNU
B42	GPIO8
B43	GPIO9
B44	PDMCLK
B44	TCPWM4_P
B45	GPIO10
B46	USB2DN2
B47	USB2DP2
B48	DNU

## abbreviation dictionary
abbreviation	long version	comment
A/D		analog-to-digital
ABS		absolute
ABUS		analog output bus
AC		alternating current
ADC		analog-to-digital converter
AES		Advanced Encryption Standard
AHB		AMBA (advanced microcontroller bus architecture) high-performance bus, an ARM® data transfer bus
Arm®		Advanced RISC Machine, a CPU architecture
API		application programming interface
APOR		analog power-on reset
BC		broadcast clock
BD		buffer descriptors
BOD		brownout detection
BOM		bill-of-materials
BR		bit rate
BRA		bus request acknowledge
BRQ		bus request
CAN		controller area network
CAN FD		controller area network with flexible data rate
CBS		credit-based shaping
CFI		canonical format indicator
CI		carry in
CMOS		complementary metal-oxide-semiconductor
CMP		compare
CO		carry out
CPHA(SPI)		clock phase
CPOL(SPI)		clock polarity
CPU		central processing unit
CPUSS		CPU subsystem
CRC		cyclic redundancy check, an error-checking protocol
CSD		CAPSENSETM sigma delta
CSV		clock supervisor
CT		continuous time
CTBm		continuous time block-mini
DAC		digital-to-analog converter
DC		direct current
DDR		double data rate (also see SDR)
DES		data encryption standard
DI		digital or data input
DMA		direct memory access
DNL		differential nonlinearity
DNU	Do not use	Do not use these connections for PCB signal routing channels. Do not connect any host system signal to these connections.
DO		digital or data output
DSI		digital signal interface
DSM		Deep Sleep mode
DW		data wire, same as P-DMA
ECC		error correcting code
ECO		external crystal oscillator
EEE		Energy Efficient Ethernet (IEEE Std 802.3az)
EEPROM		electrically erasable programmable read only memory
EMIF		external memory interface
EOF		end of frame
ETM		embedded trace macrocell
FB		feedback
FCS		frame check sequence
FIFO		first in first out
FLL		frequency locked loop
FPU		floating point unit
FSR		full scale range
GHS		Green Hills tool chain with IDE
GPIO		general purpose I/O
HCI		host-controller interface
HFCLK		high-frequency clock
HSIOM		high-speed I/O matrix
HSM		hardware security module
I2C		inter-integrated circuit
IDE		integrated development environment
IF		interface
ILO		internal low-speed oscillator
IMO		internal main oscillator
INL		integral nonlinearity
I/O		input/output
IOR		I/O read
IOW		I/O write
IP		Internet protocol
IPC		inter-processor communication
IPG		inter-packet gap
IRA		interrupt request acknowledge
IrDA		infrared interface
IRES		initial power on reset
IRQ		interrupt request
ISR		interrupt service routine
IVR		interrupt vector read
JTAG		Joint Test Action Group
L2CAP		logical link control and adaptation protocol
LAN		local area network (IEEE Std 802)
LLDP		link layer discovery protocol (IEEE Std 802.1AB)
LPCOMP		low-power comparator
LPI		low-power idle (IEEE Std 802.3az)
LRb		last received bit
LRB		last received byte
LSb		least significant bit
LSB		least significant byte
LUT		lookup table
LVD		low-voltage detection
MAC		media access control (IEEE Std 802)
MCU		microcontroller unit
MCWDT		multi-counter watchdog timer
M-DMA		memory-direct memory access
MDC		management data clock
MII		media independent interface
MISO		master-in-slave-out
MMIO		memory mapped input/output
MOSI		master-out-slave-in
MPU		memory protection unit
MSb		most significant bit
MSB		most significant byte
NC	Not connected	The connection may safely be used for routing space for a signal on a PCB. However, any signal connected to an NC pin must not have voltage levels higher than VIO.
NSP		non-standard preamble
NVIC		nested vectored interrupt controller
OTA		over-the-air programming
OTP		one-time programmable
OVD		overvoltage detection
P-DMA		peripheral-direct memory access same as DW
PC		program counter
PCH		program counter high
PCL		program counter low
PCS		physical coding sublayer
PD		power down
PFC		priority-based flow control (IEEE Std 802.1Qbb)
PGA		programmable gain amplifier
PHY		physical sublayer
PLL		phase-locked loop
PM		power management
PMA		PSOCTM memory arbiter
POR		power-on reset
PPB		private peripheral bus
PPOR		precision power-on reset
PPPoE		point-to-point protocol over ethernet
PPU		peripheral protection unit
PRNG		Pseudo-Random Number Generator
PRS		pseudo random sequence
PSRR		power supply rejection ratio
PSSDC		power system sleep duty cycle
PTP		precision time protocol (IEEE Std 1588)
PWM		pulse width modulator
RAM		random-access memory
RETI		return from interrupt
RFU	Reserved for Future use	Do not use RFU connectors for PCB routing channels so that the PCB may take advantage of future enhanced features in devices with a compatible footprint.
RF		radio frequency
RISC		reduced-instruction-set computing
ROM		read only memory
RTC		real-time clock
RW		read/write
RX		reception
SAR		successive approximation register
SC		switched capacitor
SCB		serial communication block
SCB	Serial Control Block	A peripheral that can be used as I2C, UART or SPI
SCL		I2C serial clock
SDA		I2C serial data
SDR		single data rate (also see DDR)
SE0		single-ended zero
SECDED		single error correction double error detection
SerDes		serializer/deserializer
SHA		secure hash algorithm
SHE		secure hardware extension
SFD		start of frame delimiter
SGMII		serial Gigabit media independent interface
SIE		serial interface engine
SIO		special I/O
SMIF		serial memory interface
SMPU		shared memory protection unit
SNAP		subnetwork access protocol
SNR		signal-to-noise ratio
SOF		start of frame
SOI		start of instruction
SP		stack pointer
SPD		sequential phase detector
SPI		serial peripheral interface, a communications protocol
SPI		serial peripheral interconnect
SPIM		serial peripheral interconnect master
SPIS		serial peripheral interconnect slave
SRAM		static random-access memory
SRSS		system resources sub-system
SROM		supervisory read only memory
SSADC		single slope ADC
SSC		supervisory system call
SYSCLK		system clock
SWD		single wire debug
Tbit		bit period
TC		terminal count
TCP		transfer control protocol
TCPWM		timer/counter pulse-width modulator
TD		transaction descriptors
TTL		transistor-transistor logic
TRNG		True Random Number Generator
TS		timestamp
TSU		timestamp unit
TX		transmission
UART		Universal Asynchronous Transmitter Receiver, a communications protocol
UDB		universal digital block
UDP		user datagram protocol
USB		Universal Serial Bus
USBIO		USB I/O
VLAN		Virtual LAN (IEEE Std 802.1Q)
WCO		watch crystal oscillator
WDT		watchdog timer / watchdog timer reset
WDR		watchdog reset
XIP		execute-in-place
XRES		external reset
XRES_N		external reset, active LOW
XRES_L		external reset I/O pin (active LOW)
XTAL		crystal