# command qCRC
Format: ‘qCRC:addr,length’
Meaning: Compute the CRC checksum of a block of memory using CRC-32 defined in IEEE 802.3. The CRC is computed one byte at a time, taking the most significant bit of each byte first. The initial pattern code 0xffffffff is used to ensure leading zeros affect the CRC.
Reply:
C crc32
The specified memory region’s checksum is crc32.