# command qIsAddressTagged
Format: ‘qIsAddressTagged:address’
Meaning: Check if address address is in a memory tagged region; if it is, it’s said to be tagged. The target is responsible for checking it, as this is architecture-specific.
address is the address to be checked.
Reply: Replies to this packet should all be in two hex digit format, as follows:
01
Address address is tagged.
00
Address address is not tagged.