# command z
Meaning: Remove a type breakpoint or watchpoint starting at address 'address' of kind 'kind'.
Implementation notes: A remote target shall return an empty string for an unrecognized breakpoint or watchpoint packet type. A remote target shall support either both or neither of a given ‘Ztype…’ and ‘ztype…’ packet pair. To avoid potential problems with duplicate packets, the operations should be implemented in an idempotent way.
## software breakpoint
Format: ‘z0,addr,kind’
Meaning: Remove a software breakpoint at address addr of type kind.
The kind is target-specific and typically indicates the size of the breakpoint in bytes that should be inserted. E.g., the ARM and MIPS can insert either a 2 or 4 byte breakpoint. Some architectures have additional meanings for kind; if no architecture-specific value is being used, it should be ‘0’. kind is hex-encoded.
Reply:
OK
## hardware breakpoint
Format: ‘z1,addr,kind’
Meaning: Remove a hardware breakpoint at address addr.
A hardware breakpoint is implemented using a mechanism that is not dependent on being able to modify the target’s memory.
The kind is target-specific and typically indicates the size of the breakpoint in bytes that should be inserted. E.g., the ARM and MIPS can insert either a 2 or 4 byte breakpoint. Some architectures have additional meanings for kind; if no architecture-specific value is being used, it should be ‘0’. kind is hex-encoded.
Implementation note: A hardware breakpoint is not affected by code movement.
Reply:
OK
## write watchpoint
Format: ‘z2,addr,kind’
Meaning: Remove a write watchpoint at addr. The number of bytes to watch is specified by kind.
Reply:
OK
## read watchpoint
Format: ‘z3,addr,kind’
Meaning: Remove a read watchpoint at addr. The number of bytes to watch is specified by kind.
Reply:
OK
## access watchpoint
Format: ‘z4,addr,kind’
Meaning: Remove an access watchpoint at addr. The number of bytes to watch is specified by kind.
Reply:
OK