# SPI
Different variants exist. Usually SPI refers to the Motorola Serial Peripheral Interface. Other variants are the Texas Instruments Serial protocol (SSP) and the National Instruments Microwire.
## Modes
There are 4 Modes. Defied by the two settings “clock polarity” CPOL and “clock phase” CPHA.
“clock polarity” CPOL = 0:
Clock line is low when idle.
“clock polarity” CPOL = 1:
Clock line is high when idle.
“clock phase” CPHA = 0:
1. first data bit is output on /CS activating (going low).
2. data bits change when clock goes to idle level.
3. data bits are read when clock comes from idle level.
“clock phase” CPHA = 1:
1. first data bit starts on first edge after /CS activates.
2. data bits change when clock comes from idle level.
3. data bits are read when clock goes to idle level.
mode	CPOL	CPHA	write bit	read bit
0	0	0	falling clock, and when /CS activates	rising clock
1	0	1	rising clock	falling clock
2	1	0	rising clock, and when /CS activates	falling clock
3	1	1	falling clock	rising clock

## API
The part “signal_name” in the described functions will be replaced by the name of the signal. E.g. if your signal is called “audio” then the API function “signal_name_transfer” will become “audio_transfer”.
void signal_name_transfer(const uint8_t *data_send,
        const uint8_t *data_receive,
        const uint32_t length )
Will send “length” bytes from the buffer “data_send” out on MOSI and will receive the same amount of bytes from MISO into the buffer “data_receive”.