# STM32F429
ARM Cortex-M4 (180MHz) FPU
## Memory Map
start address	end address	used for	comment
0x0	0x1fffff		Aliased to flash, system memory or SRAM depending on the BOOT pins
0x20 0000	0x7ff ffff	reserved
0x800 0000	0x81f ffff	flash memory
0x820 0000	0xfff ffff	reserved
0x1000 0000	0x1000 ffff	CCM data RAM	64 KB SRAM
0x1001 0000	0x1ffe bfff	reserved
0x1ffe c000	0x1fff c00f	option bytes
0x1fff c010	0x1ffe ffff	reserved
0x1fff 0000	0x1fff 7a0f	system memory
0x1fff 7a10	0x1fff 7fff	reserved
0x1fff c000	0x1fff c00f	option bytes
0x1fff c010	0x1fff ffff	reserved
0x2000 0000	0x2001 bfff	SRAM 112KB
0x2001 C000	0x2001 ffff	SRAM 16 KB
0x2002 0000	0x2002 ffff	SRAM 64 KB
0x2003 0000	0x3fff ffff	reserved
0x4000 0000	0x4000 7fff	APB1
0x4000 0000	0x4000 03ff	TIM2
0x4000 0400	0x4000 07ff	TIM3
0x4000 0800	0x4000 0bff	TIM4
0x4000 0c00	0x4000 0fff	TIM5
0x4000 1000	0x4000 13ff	TIM6
0x4000 1400	0x4000 17ff	TIM7
0x4000 1800	0x4000 1bff	TIM12
0x4000 1c00	0x4000 1fff	TIM13
0x4000 2000	0x4000 23ff	TIM14
0x4000 2400	0x4000 27ff	reserved
0x4000 2800	0x4000 2bff	RTC & BKP Registers
0x4000 2c00	0x4000 2fff	WWDG
0x4000 3000	0c4000 33ff	IWDG
0x4000 3400	0x4000 37ff	I2S2ext
0x4000 3800	0x4000 3bff	SPI2 / I2S2
0x4000 3c00	0x4000 3fff	SPI3 / I2S3
0x4000 4000	0x4000 43ff	I2S3ext
0x4000 4400	0x4000 47ff	USART2
0x4000 4800	0x4000 4bff	USART3
0x4000 4c00	0x4000 4fff	UART4
0x4000 5000	0x4000 53ff	UART5
0x4000 5400	0x4000 5700	I2C1
0x4000 5800	0x4000 5bff	I2C2
0x4000 5c00	0x4000 5fff	I2C3
0x4000 6000	0x4000 63ff	reserved
0x4000 6400	0x4000 67ff	CAN1
0x4000 6800	0x4000 6bff	CAN2
0x4000 6c00	0x4000 6fff	reserved
0x4000 7000	0x4000 73ff	PWR
0x4000 7400	0x4000 77ff	DAC
0x4000 7800	0x4000 7bff	UART7
0x4000 7c00	0x4000 7fff	UART8
0x4000 8000	0x4000 ffff	reserved
0x4001 0000	0x4001 6bff	APB2
0x4001 0000	0x4001 03ff	TIM1
0x4001 0400	0x4001 07ff	TIM8
0x4001 0800	0x4001 0fff	reserved
0x4001 1000	0x4001 13ff	USART1
0x4001 1400	0x4001 17ff	USART6
0x4001 1800	0x4001 1fff	reserved
0x4001 2000	0x4001 23ff	ADC1 - ADC2 - ADC3
0x4001 2400	0x4001 2bff	reserved
0x4001 2c00	0x4001 2fff	SDIO
0x4001 3000	0x4001 33ff	SPI1
0x4001 3400	0x4001 37ff	SPI4
0x4001 3800	0x4001 3bff	SYSCFG
0x4001 3c00	0x4001 3fff	EXTI
0x4001 4000	0x4001 43ff	TIM9
0x4001 4400	0x4001 47ff	TIM10
0x4001 4800	0x4001 4bff	TIM11
0x4001 4c00	0x4001 4fff	reserved
0x4001 5000	0x4001 53ff	SPI5
0x4001 5400	0x4001 57ff	SPI6
0x4001 5800	0x4001 5bff	SAI1
0x4001 5c00	0x4001 67ff	reserved
0x4001 6800	0x4001 6bff	LCD-TFT
0x4001 6c00	0x4001 ffff	reserved
0x4002 0000	0x4007 ffff	AHB1
0x4002 0000	0x4002 03ff	GPIOA
0x4002 0400	0x4002 07ff	GPIOB
0x4002 0800	0x4002 0bff	GPIOC
0x4002 0c00	0x4002 0fff	GPIOD
0x4002 1000	0x4002 13ff	GPIOE
0x4002 1400	0x4002 17ff	GPIOF
0x4002 1800	0x4002 1bff	GPIOG
0x4002 1c00	0x4002 1fff	GPIOH
0x4002 2000	0x4002 23ff	GPIOI
0x4002 2400	0x4002 27ff	GPIOJ
0x4002 2800	0x4002 2bff	GPIOK
0x4002 2c00	0x4002 2fff	reserved
0x4002 3000	0x4002 33ff	CRC
0x4002 3400	0x4002 37ff	reserved
0x4002 3800	0x4002 3bff	RCC
0x4002 3c00	0x4002 3fff	Flash interface register
0x4002 4000	0x4002 4fff	BKPSRAM
0x4002 5000	0x4002 5fff	reserved
0x4002 6000	0x4002 63ff	DMA1
0x4002 6400	0x4002 67ff	DMA2
0x4002 6800	0x4002 7fff	reserved
0x4002 8000	0x4002 83ff	Ethernet MAC
0x4002 8400	0x4002 87ff	Ethernet MAC
0x4002 8800	0x4002 8bff	Ethernet MAC
0x4002 8c00	0x4002 8fff	Ethernet MAC
0x4002 9000	0x4002 93ff	Ethernet MAC
0x4002 9400	0x4002 afff	reserved
0x4002 b000	0x4002 bbff	DMA2D
0x4002 bc00	0x4003 ffff	reserved
0x4004 0000	0x4007 ffff	USB OTG HS
0x4008 0000	0x4fff ffff	reserved
0x5000 0000	0x5006 0bff	AHB2
0x5000 0000	0x5003 ffff	USB OTG FS
0x5004 0400	0x5004 ffff	reserved
0x5005 0000	0x5005 03ff	DCMI
0x5005 0400	0x5006 07ff	reserved
0x5006 0800	0x5006 0bff	RNG
0x5006 0c00	0x5fff ffff	reserved
0x6000 0000	0xdfff ffff	AHB3
0x6000 0000	0x6fff ffff	FMC bank 1
0x7000 0000	0x7fff ffff	FMC bank 2
0x8000 0000	0x8fff ffff	FMC bank 3
0x9000 0000	0x9fff ffff	FMC bank 4
0xa000 0000	0xa000 0fff	FMC control register
0xa000 1000	0xbfff ffff	reserved
0xc000 0000	0xcfff ffff	FMC bank 5
0xd000 0000	0xdfff ffff	FMC bank 6
0xe000 0000	0xe00f ffff	Cortex-M4 internal peripherals
0xe010 0000	0xffff ffff	reserved

## Peripherals
### IRQ
IRQ Number	Signal	Description
0	WWDG	Window WatchDog
1	PVD	PVD through EXTI Line detection
2	TAMP_STAMP	Tamper and TimeStamps through the EXTI line
3	RTC_WKUP	RTC Wakeup through the EXTI line
4	FLASH	FLASH Handler
5	RCC_IRQHandler	RCC
6	EXTI0	EXTI Line0
7	EXTI1	EXTI Line1
8	EXTI2	EXTI Line2
9	EXTI3	EXTI Line3
10	EXTI4	EXTI Line4
11	DMA1_Stream0	DMA1 Stream 0
12	DMA1_Stream1	DMA1 Stream 1
13	DMA1_Stream2	DMA1 Stream 2
14	DMA1_Stream3	DMA1 Stream 3
15	DMA1_Stream4	DMA1 Stream 4
16	DMA1_Stream5	DMA1 Stream 5
17	DMA1_Stream6	DMA1 Stream 6
18	ADC	ADC1, ADC2 and ADC3s
19	CAN1_TX	CAN1 TX
20	CAN1_RX0	CAN1 RX0
21	CAN1_RX1	CAN1 RX1
22	CAN1_SCE	CAN1 SCE
23	EXTI9_5	External Line[9:5]s
24	TIM1_BRK_TIM9	TIM1 Break and TIM9
25	TIM1_UP_TIM10	TIM1 Update and TIM10
26	TIM1_TRG_COM_TIM11	TIM1 Trigger and Commutation and TIM11
27	TIM1_CC	TIM1 Capture Compare
28	TIM2	TIM2
29	TIM3	TIM3
30	TIM4	TIM4
31	I2C1_EV	I2C1 Event
32	I2C1_ER	I2C1 Error
33	I2C2_EV	I2C2 Event
34	I2C2_ER	I2C2 Error
35	SPI1	SPI1
36	SPI2	SPI2
37	USART1	USART1
38	USART2	USART2
39	USART3	USART3
40	EXTI15_10	External Line[15:10]s
41	RTC_Alarm	RTC Alarm (A and B) through EXTI Line
42	OTG_FS_WKUP	USB OTG FS Wakeup through EXTI line
43	TIM8_BRK_TIM12	TIM8 Break and TIM12
44	TIM8_UP_TIM13	TIM8 Update and TIM13
45	TIM8_TRG_COM_TIM14	TIM8 Trigger and Commutation and TIM14
46	TIM8_CC	TIM8 Capture Compare
47	DMA1_Stream7	DMA1 Stream7
48	FMC	FMC
49	SDIO	SDIO
50	TIM5	TIM5
51	SPI3	SPI3
52	UART4	UART4
53	UART5	UART5
54	TIM6_DAC	TIM6 and DAC1&2 underrun errors
55	TIM7	TIM7
56	DMA2_Stream0	DMA2 Stream 0
57	DMA2_Stream1	DMA2 Stream 1
58	DMA2_Stream2	DMA2 Stream 2
59	DMA2_Stream3	DMA2 Stream 3
60	DMA2_Stream4	DMA2 Stream 4
61	ETH	Ethernet
62	ETH_WKUP	Ethernet Wakeup through EXTI line
63	CAN2_TX	CAN2 TX
64	CAN2_RX0	CAN2 RX0
65	CAN2_RX1	CAN2 RX1
66	CAN2_SCE	CAN2 SCE
67	OTG_FS	USB OTG FS
68	DMA2_Stream5	DMA2 Stream 5
69	DMA2_Stream6	DMA2 Stream 6
70	DMA2_Stream7	DMA2 Stream 7
71	USART6	USART6
72	I2C3_EV	I2C3 event
73	I2C3_ER	I2C3 error
74	OTG_HS_EP1_OUT	USB OTG HS End Point 1 Out
75	OTG_HS_EP1_IN	USB OTG HS End Point 1 In
76	OTG_HS_WKUP	USB OTG HS Wakeup through EXTI
77	OTG_HS	USB OTG HS
78	DCMI	DCMI
79	reserved	reserved
80	HASH_RNG	Hash and Rng
81	FPU	FPU
82	UART7	UART7
83	UART8	UART8
84	SPI4	SPI4
85	SPI5	SPI5
86	SPI6	SPI6
87	SAI1	SAI1
88	LTDC	LTDC
89	LTDC_ER	LTDC_ER
90	DMA2D	DMA2D

### Clocks
### UART
### GPIO
#### Function select
# Nucleo-F429ZI board
## pinout
GPIO	Signal	description
B0	LD1	LED green
B7	LD2	LED blue
B14	LD3	LED red
D8	UART3 TX	connected to ST-Link
D9	UART3 RX	connected to ST-Link
A1	RMII_REF_CLK	Ethernet RMII
A2	RMII_MDIO	Ethernet RMII
C1	RMII_MDC	Ethernet RMII
A7	RMII_MII_CRS_DV / RMII RX Data Valid	Ethernet RMII
C4	RMII_MII_RXD0	Ethernet RMII
C5	RMII_MII_RXD1	Ethernet RMII
G11	RMII_MII_TX_EN	Ethernet RMII
G13	RMII_MII_TXD0	Ethernet RMII
B13	RMII_MII_TXD1	Ethernet RMII

## User LED
### LD1 (green)
PB0 (leuchtet wenn GPIO = 1 = High)
Kann auch auf PA5 verbunden werden per solderbridge
### LD2 (blue)
PB7 (leuchtet wenn GPIO = 1 = High)
### LD3 (red)
PB14 (leuchtet wenn GPIO = 1 = High)
## Ethernet
10/100 Mbit/s, PHY generates 50 MHz RMII_REF_CLK.
## abbreviation dictionary
abbreviation	long version	comment
rw	read/write	Software can read and write to these bits.
r	read-only	Software can only read these bits.
w	write-only	Software can only write to this bit. Reading the bit returns the reset value.
rc_w1	read/clear	Software can read as well as clear this bit by writing 1. Writing ‘0’ has no effect on the bit value.
rc_w0	read/clear	Software can read as well as clear this bit by writing 0. Writing ‘1’ has no effect on the bit value.
rc_r	read/clear by read	Software can read this bit. Reading this bit automatically clears it to ‘0’. Writing ‘0’ has no effect on the bit value.
rs	read/set	Software can read as well as set this bit. Writing ‘0’ has no effect on the bit value.
rt_w	read-only write trigger	Software can read this bit. Writing ‘0’ or ‘1’ triggers an event but has no effect on the bit value.
t	toggle	Software can only toggle this bit by writing ‘1’. Writing ‘0’ has no effect.
Res.	Reserved	Reserved bit, must be kept at reset value.